International Scientific Conference

on

AGRICULTURAL WATER MANAGEMENT

AND MECHANIZATION

## FACTORS FOR SUSTAINABLE AGRICULTURE

Sofia, 8th – 10th October 2003

# Global warming and irrigation development.

## A world-wide view

Daniele De Wrachien *

# EurAgEng President

Chairman Field of Interest on Soil and Water

Head of the Department of Agricultural Hydraulics, State University of Milan, Italy

Summary

Most of the world’s irrigation systems were developed on a step-by-step basis over the centuries and were designed for a long life (50 years or more) on the assumption that climatic conditions would not change in the future. This will not be so in the years to come due to global warming and the greenhouse effect. Therefore, engineers and decision-makers need to systematically review planning principles, design criteria, operating rules, contingency plans and management policies for new infrastructures.

In relation to these issues and based on available information, this report gives an overview of current and future (time horizon 2025) irrigation development around the world. Moreover, the paper analyses the results of the most recent and advanced General Circulation Models for assessing the hydrological impacts of climate variability on crop requirements, water availability and the planning and design process of irrigation systems. Finally, a five-step planning and design procedure is proposed that is able to integrate, within the development process, the hydrological consequences of climate change.

*Correspondence to D. De Wrachien Department of Agricultural Hydraulics, State University of Milan, Via Celoria 2, 20133 Milano (e-mail: daniele.dewrachien@unimi.it)

- Introduction

Agriculture will have to meet the future challenges posed by food security by increasing production while conserving natural resources.

In the past, the increased demand for food has been satisfied by the expansion of agricultural land. Today, the prospects of increasing the gross cultivated area, in both the developed and developing countries, are limited by the dwindling number of economically attractive sites for new large-scale irrigation and drainage projects. Therefore, any increase in agricultural production will necessarily rely largely on a more accurate estimation of crop water requirements on the one hand, and on major improvements in the operation, management and performance of existing irrigation and drainage systems, on the other.

The failings of present systems and the inability to sustainably exploit surface and ground water resources can be attributed essentially to poor planning, design, systems management and development.

With a population that is expected to grow from 6 billion today to at least 8 billion by the year 2025, bold measures are essential if the problems of irrigation systems and shortage of food are to be avoided.

All the above factors and constraints compel decision-makers to review the strengths and weaknesses of current trends in irrigation and drainage and rethink technology, institutional and financial patterns, research thrust and manpower policy so that service levels and system efficiency can be improved in a sustainable manner.

- Irrigation Development and the Global Food Challenge

To solve the above problems massive investments have been made over the last few decades by governments and individuals and a concerted effort by the international Community. The challenge was to provide enough food for 2 billion more people, while increasing domestic and industrial water demand. Different scenarios have been developed to explore a number of issues, such as the expansion of irrigated agriculture, massive increases in food production from rainfed lands, water productivity trends and public acceptance of genetically modified crops. Opinions differ among the experts as to some of the above issues. However, there is broad consensus that irrigation can contribute substantially to increasing food production.

Today, the world’s food production comes from a cultivated area of about 1.5 billion ha, representing 12% of the total land area (Schultz and De Wrachien, 2002).  About 1.1 billion ha of cultivated land have no water management systems, though this area supplies 45% of food production. At present irrigation covers 270 million ha, i.e. 18% of the world’s arable land. Overall, irrigated land contributes to 40% of agricultural output and employs about 30% of population in rural areas. It uses about 70% of water withdrawn from global river systems. About 60% of this water is used consumptively, the rest returning to the river systems. Drainage of rainfed crops covers about 130 million ha, i.e. 9% of the world’s arable land. In about 60 million ha of the irrigated lands there is a drainage system, as well. The 130 million or so hectares of drained rainfed land produces around 15% of crop output.

  - Developments in Irrigation

Over the last forty years irrigation has been a major contributor to the growth of food and fiber supply for a global population that has more than doubled, from 3 to over 6 billion people. Global irrigated area increased by around 2% a year in the 1960s and ‘70s, slowing down to around 1% in the ’80s, and lower still in the ’90s. Between 1965 and 1995 the world’s irrigated land grew from 150 to 260 million ha. Nowadays it is increasing at a very slow rate because of the significant slowdown in new investments, combined with the loss of irrigated areas due to salination and urban encroachment.

Notwithstanding these achievements, today the majority of agricultural land (1.1 billion ha) still has no water management system. In this context it is expected that 90% of the increase in food production will have to come from existing cultivated land and only 10% from conversion from other uses. In the rainfed areas with no water management systems some improvements can be achieved with water harvesting and watershed management. However, in no way can the cultivated area with no water management contribute significantly to the required increase in food production. For this reason, the share of irrigated and drained areas in food production will have to increase. This can be achieved either by installing irrigation or drainage facilities in the areas without a system or by improving and modernizing existing systems. The International Commission on Irrigation and Drainage (ICID) estimates that within the next 25 years, this process may result in a shift of the contribution to the total food production to around 30% for the areas with no water management system, 50% for the areas with an irrigation system and 20% for the rainfed areas with a drainage system (Schultz, 2002).

  - The Global Food Challenge

As the world population continues to grow so too does the need to constantly increases food production. Several actions are required to cope with this increasing demand. Globally, the core challenge must be to improve water productivity. Where land is limiting, yields per unit area must also be enhanced. These measures lead to two basic development directions (van Hofwegen and Svendsen, 2000):

- increasing the yield frontier in those areas where present levels of production are close to their potential;

- closing the yield gap where considerable production gains can be achieved with current technology.

Based on the above assumptions, three models of food and irrigation water demand have been developed by non governmental organizations for the time horizon 2025 (Plusquellec, 2002). These three models predict that present irrigated agriculture would have to increase by 15-22%. Moreover, water withdrawals for irrigation are also expected to increase at unprecedented rates, a major challenge considering that environmentalists argue that irrigation withdrawals should be reduced, as they have great expectations in the potential of biotechnology in agriculture.

Although the scenarios differ considerably, it is generally agreed that the world is entering the twenty-first century on the brink of a new food crisis, as ominous, but far more complex, that the famine it faced in the 1960s. Some analysts believe that what is needed is a new and “greener revolution” to increase productivity again and boost production. But the challenges are far more complex than simply producing more food, because global conditions have changed since the green revolution years.

- Climate Change and Irrigation Requirements

Agriculture is a human activity that is intimately associated with climate. It is well known that the broad patterns of agricultural growth over long time scales can be explained by a combination of climatic, ecological and economic factors. Modern agriculture has progressed by weakening the downside risk of these factors through irrigation, the use of pesticides and fertilizers, the substitution of human labor with energy intensive devices, and the manipulation of genetic resources. A major concern in the understanding of the impacts of climate change is the extent to which world agriculture will be affected. Thus, in the long term, climate change is an additional problem that agriculture has to face in meeting global and national food requirements. This recognition has prompted recent advances in the coupling of global vegetation and climate models.

In the last decade, global vegetation models have been developed that include parameterizations of physiological processes such as photosynthesis, respiration, transpiration and soil water in-take (Bergengren et al., 2001). These tools have been coupled with General Circulation Models (GCMs) and applied to both paleoclimatic and future scenarios (Doherty et al., 2000, Levis et al. 2000). The use of physiological parameterizations allows these models to include the direct effects of changing CO levels on primary productivity and competition, along with the crop water requirements. In the next step the estimated crop water demands could serve as input to agro-economic models which compute the irrigation water requirements (IR), defined as the amount of water that must be applied to the crop by irrigation in order to achieve optimal crop growth.

On the global scale, scenarios of future irrigation water use have been developed by Seckler et al. (1997) and Alcamo et al. (2000). Alcamo et al. employed the raster-based Global Irrigation Model (GIM) of Döll and Siebert (2001), with a spatial resolution of 0.5 by 0.5. This model represents one of the most advanced tools today available for exploring the impact of climate change on IR at worldwide level.

More recently, the GIM has been applied to explore the impact of climate change on the irrigation water requirements of those areas of the globe equipped for irrigation in 1995 (Döll, 2002). Estimates of long-term average climate change have been taken from two different GCMs:

- the Max Planck Institute for Meteorology (MPI-ECHAM4), Germany

- the Hadley Centre for Climate Prediction and Research (HCCPR-CM3), UK

The following climatic conditions have been computed:

- present-day long-term average climatic conditions, i.e. the climate normal 1961-1990 (baseline climate);

- future long-term average climatic conditions of the 2020s and 2070s (climatic change).

For the above climatic conditions, the GIM computed both the net and gross irrigation water requirements in all 0.5 by 0.5 raster cells with irrigated areas. “Gross irrigation requirement” is the total amount of water that must be applied such that evapotraspiration may occur at the potential rate and optimum crop productivity may be achieved. Only part of the irrigated water is actually used by the plant and evapotranspirated. This amount, i.e. the difference between the potential evapotranspiration and the evapotranspiration that would occur without irrigation, represents the “net irrigation requirement”, IRnet.

The simulations show that irrigation requirements increase in most irrigated areas north of 40°N, by up to 30%, which is mainly due to decreased precipitation, in particular during the summer. South of this latitude, the pattern becomes complex. For most of the irrigated areas of the arid northern part of Africa and the Middle East, IRnet diminishes. In Egypt, a decrease of about 50% in the southern part is accompanied by an increase of about 50% in the central part. In central India, baseline IRnet values of 250-350mm are expected to more than double by the 2020s. In large parts of China the impact of climate change is negligible (less than 5%), with decreases in northern China, as precipitation is assumed to increase. When the cell-specific net irrigation requirements are summed up over the world regions, increases and decreases of the cell values caused by climate change almost average out, increasing by 3.3% in the 2020s and by 5.5% in the 2070s.

The simulations also show that in areas equipped for irrigation in 1995 IRnet is likely to increase in 66% of these areas by the 2020s and in 62% by the 2070s.

- Climate Change and Water Availability

In order to assess the problem of water scarcity, the appropriate averaging units are not world regions but river basins.

Climate predictions from four state-of-the-art General Circulation Models were used to assess the hydrologic sensitivity to climate change of nine large, continental river basins (Nijssen et al., 2001). The river basins were selected on the basis of the desire to represent a range of geographic and climatic conditions. Four models have been used:

- the Hadley Centre for Climate Prediction and Research (HCCPR-CM2), UK

- the Hadley Centre for Climate Prediction and Research (HCCPR-CM3), UK

- the Max Planck Institute for Meteorology (MPI-ECHAM4), Germany

- the Department of Energy (DOE-PCM3), USA

All predicted transient climate response to changing greenhouse gas concentrations and incorporated modern land surface parameterizations. The transient emission scenarios differ slightly from one model to another, partly because they represent greenhouse gas chemistry differently.

Changes in basin-wide, mean annual temperature and precipitation were computed for three decades in the transient climate model runs ( 2025, 2045 and 2095) and hydrologic model simulations were performed for decades centered on 2025 and 2045.

The main conclusions are summarized below.

- All models predict a warming for all nine basins, but the amount of warming varies widely between the models, especially for the longer time horizon. The greatest warming is predicted to occur during the winter months in the highest latitudes. Precipitation generally increases for the northern basins, but the signal is mixed for basins in the mid-latitudes and tropics, although on average slight precipitation increases are predicted.

- The largest changes in hydrological cycle are predicted for the snow-dominated basins of mid to higher latitudes, as a result of the greater amount of warming that is predicted for these regions. The presence or absence of snow fundamentally changes the water balance, due to the fact that water stored as snow during the winter does not become available for runoff or evapotranspiration until the following spring’s melt period.

- Globally, the hydrological response predicted for most of the basins in response to the GCMs predictions is a reduction in annual streamflow in the tropical and mid-latitudes. In contrast, high-latitude basins tend to show an increase in annual runoff, because most of the predicted increase in precipitation occurs during the winter, when the available energy is insufficient for an increase in evaporation. Instead, water is stored as snow and contributes to streamflow during the subsequent melt period.

- Planning and Design of Irrigation Systems under Climate Change

Uncertainties as to how the climate will change and how irrigation systems will have to adapt to these changes, are challenges that planners and designers will have to cope with. In view of these uncertainties, planners and designers need guidance as to when the prospect of climate change should be embodied and factored into the planning and design process (De Wrachien and Feddes, 2003). An initial question is whether, based on GCM results or other analyses, there is reason to expect that a region’s climate is likely to change significantly during the life of a system. If significant climate change is thought to be likely, the next question is whether there is a basis for forming an expectation about the likelihood and nature of the change and its impacts on the infrastructures.

The suitability and robustness of an infrastructure can be assessed either by running “what if“ scenarios that incorporate alternative climates or through synthetic hydrology by translating apparent trends into enhanced persistence.

When there are grounds for formulating reasonable expectations about the likelihood of climate changes, the relevance of these changes will depend on the nature of the project under consideration. Climate changes that are likely to occur several decades from now will have little relevance for decisions involving infrastructure development or incremental expansion of existing facilities’ capacity. Under these circumstances planners and designers should evaluate the options under one or more climate change scenario to determine the impacts on the project’s net benefits. If the climate significantly alters the net benefits, the costs of proceeding with a decision assuming no change can be estimated. If these costs are significant, a decision tree can be constructed for evaluating the alternatives under two or more climate scenarios (Hobbs, et al., 1997). Delaying an expensive and irreversible project may be a competitive option, especially in view of the prospect that the delay will result in a better understanding as to how the climate is likely to change and impact the effectiveness and performance of the infrastructure.

Aside from the climate change issue, the high costs of and limited opportunities for developing new large scale projects, have led to a shift away from the traditional, fairly inflexible planning principles and design criteria for meeting changing water needs and coping with hydrological variability and uncertainty. Efficient, flexible works designed for current climatic trends would be expected to perform efficiently under different environmental conditions. Thus, institutional flexibility that might complement or substitute infrastructure investments is likely to play an important role in irrigation development under the prospect of global climatic change. Frederick et al. (1997) proposed a five-step planning and design process for water resource systems, for coping with uncertain climate and hydrologic events, and potentially suitable for the development of large irrigation schemes.

If climate change is recognized as a major planning issue (first step), the second step in the process would consist of predicting the impacts of climate change on the region’s irrigated area. The third step involves the formulation of alternative plans, consisting of a system of structural and/or non-structural measures and hedging strategies, that address, among other concerns, the projected consequences of climate change. Non-structural measures that might be considered include modification of management practices, regulatory and pricing policies. Evaluation of the alternatives, in the fourth step, would be based on the most likely conditions expected to exist in the future with and without the plan. The final step in the process involves comparing the alternatives and selecting a recommended development plan.

The planning and design process needs to be sufficiently flexible to incorporate consideration of and responses to many possible climate impacts. Introducing the potential impacts of and appropriate responses to climate change in planning and design of irrigation systems can be both expensive and time consuming. The main factors that mighty influence the worth of incorporating climate change into the analysis are the level of planning (local, national, international), the reliability of GCMs, the hydrologic conditions, the time horizon of the plan or life of the project.

- Concluding Remarks

- Agriculture will have to meet the future challenges posed by food security by increasing production while conserving natural resources.

- With a population that is expected to grow from 6 billion today to at least 8 billion by the year 2025, bold measures are essential if the problems of irrigation systems and shortage of food are to be avoided.

- Different scenarios have been developed to explore a number of issues, such as the expansion of irrigated agriculture, massive increases in food production from rainfed lands and water productivity trends. Opinions differ among experts as to some of the above issues. However, there is broad consensus that irrigation can contribute substantially to increasing food production in the years to come.

- Most of the world’s irrigation systems were developed on a step-by-step basis, over the centuries and were designed for a long life (50 years or more), on the assumption that climatic conditions would not change. This will not be so in the future, due to global warming and the greenhouse effect. Therefore, engineers and decision-makers need to systematically review planning principles, design criteria, operating rules, contingency plans and water management policies.

- Uncertainties as to how the climate will change and how irrigation systems will have to adapt to these changes are issues that water authorities are compelled to address. The challenge is to identify short-term strategies to cope with long-term uncertainties. The question is not what is the best course for a project over the next fifty years or more, but rather, what is the best direction for the next few years, knowing that a prudent hedging strategy will allow time to learn and change course.

- The planning and design process needs to be sufficiently flexible to incorporate consideration of and responses to many possible climate impacts. The main factors that will influence the worth of incorporating climate change into the process are the level of planning, the reliability of the forecasting models, the hydrological conditions and the time horizon of the plan or the life of the project.

- The development of a comprehensive approach that integrates all these factors into irrigation project selection, requires further research on the processes governing climate changes, the impacts of increased atmospheric carbon dioxide on vegetation and runoff, the effect of climate variables on crop water requirements and the impacts of climate on infrastructure performance.

References

Alcamo J., Henrish T., Rösch T. 2000. World Water in 2025. Global Modeling and Scenario Analysis for the World Commission on Water for the 21st Century. Kassel World Water Series Report 2. Centre for Environmental Systems Research, University of Kassel, Germany.

Bergengren J.C., Thompson S.L., Pollard D., Deconto R.M. 2001. Modeling global climate-vegetation interactions in a doubled CO world. Climatic Change, 50, 31-75.

De Wrachien D., Feddes R. 2003. Drainage and land reclamation in a changing environment Overview and challenges. Invited keynote lecture. International Conference on Land Reclamation and Water Resources Development May, Mantua, Italy.

Doherty R., Kutzbach J., Foley I., Pollard D. 2000. Fully-compled climate/dynamical vegetation model simulation over northern Africa during mid-Holocene. Clim Dyn, 16, 561-573

Döll P. 2002. Impact of climate change and variability on irrigation requirements. A global perspective. Climatic Change, 54, 269-293.

Döll P, Siebert S. 2001. Global modeling of irrigation water requirements. Water Resources Research, 38, 8-1, 8-11.

Frederick K.D., Major D.C., Stakhiv E.Z. 1997. Water resources planning principles and evaluation criteria for climate change. Climatic Change, 37, 1-313.

Hobbs B.F., Chao P.T., Venkatesh B.M. 1997. Using decision analysis to include climate change in water resources in decision making. Climatic Change, 37, 177-202.

Hofwegen P.J.M. van, Svendsen M. 2000. A Vision of Water for Food and Rural Development. The Hague, The Netherlands.

Levis S., Foley J.A., Pollard D. 2000. Large-scale vegetation feedbacks on a doubled CO climate. Journal Climate. 13, 1313-1325.

Nijssen B., O’Donnell G.M., Hamlet A.F., Lettenmaier D.P. 2001. Hydrologic sensitivity of global rivers to climate change Climatic Change, 50, 143-175.

Plusquellec H. 2002. Is the daunting challenge of irrigation achievable. Irrigation and Drainage, 51, 185-198.

Seckler D., Amarasinghe V., Molden D., de Silva R., Barker R. 1997. World Water Demand and Supply 1990 to 2025. Scenarios and Issues. Research Report 19, IWMI, Colombo. Sri Lanka.

Schultz B. 2002. Opening address. In Proceedings of the 18th Congress on Irrigation and Drainage (ICID). July, Montreal, Canada.

Schultz B., De Wrachien D. 2002. Irrigation and drainage systems. Research and development in the 21st century. Irrigation and Drainage, 51, 311-327.