Emission Factor Report (ID: 421097)

| Administrative information |
| --- |
| Data Provider: | Annamaria Costa |
| Data Provider Country: | Italy |
| Data Provider Contact: | ipcc-efdb@iges.or.jp |
| Date calculated: | Unknown |
| Date submitted to EFDB by Data Provider: | 2009-06-09 00:00:00 |
| Date posted to EFDB by IPCC: | 05/03/2010 |

| Technical information |
| --- |
| Gas: | NITROUS OXIDE |
| IPCC 1996 Source/Sink Category: | Agriculture (4) -> Manure Management (4B) -> Swine (4B8) |
| IPCC 2006 Source/Sink Category: | Agriculture, Forestry, and Other Land Use (3) -> Livestock (3.A) -> Manure Management (3.A.2) -> Swine (3.A.2.h) |
| Properties |  |
| Technologies/Practices: | Indoor intensive pig rearing |
| Abatement/Control Technologies: | Vacuum system manure removal (BAT or Best Available Technique to reduce pollutants emission) |
| Parameters/Conditions: | Mechanically ventilated swine building, ventilation rate is monitored in continuous by the system FANCOM Easy Flow. |
| Region/Regional Conditions: | Applicable in regions with a temperate climate, similar to Italy (outside temperature ranged from a minimum of 2 degrees centigrade in winter to 35 degrees centigrade in summer). Outside temperature is essential to determine the inside temperature of the animal house and so the ventilation rate responsible of pollutants inside concentration and emission to the atmosphere |
| Others: |  |
| Description: | Emission factor for nitrous oxide(N2O) from manure management from swine husbandry |
| Value: | [A] 0.06 (weaning); [B] 2.55 (farrowing); [C] 0.15 (fattening); [D] 0.40 (gestating sows) |
| Unit: | kg/animal/yr |
| Value in common units: |  |
| Common unit: |  |
| Equation: |  |
| IPCC Worksheet: |  |
| Source of data: | Peer-reviewed paper |
| Technical Reference: | Costa A. and M. Guarino. Definition of yearly emission factor of dust and greenhouse gases through continuous measurements in swine husbandry. Atmospheric Environment, 43, 1548-1556; |
| Reference language: | English |
| Abstract in English: | The object of this study was to develop an accurate estimation method to evaluate the contribution of the various compartments of swine husbandry to dust and GHG (greenhouse gases, CO2, CH4 and N2O) emission into the atmosphere during one year of observation. A weaning, a gestation, a farrowing and a fattening room in an intensive pig house were observed in three different periods (Autumn - Winter, Springtime and Summer, monitoring at least 60 % of each period (20 % at the beginning, in the middle and at the end) of each cycle. During monitoring, live weight, average live weight gain, number of animals and its variation, type of feed and feeding time were taken into account to evaluate their influence on PM10, or the fraction of suspended particulate matter with an aerodynamic diameter less than or equal to 10 µm (Emission Inventory Guidebook, 2008) and to define GHG emission. The selected piggery had a ventilation control system using a free running impeller to monitor continuously real-time environmental and management parameters with an accuracy of 5%. PM10 concentration was monitored by a sampler (Haz Dust- EPAM 5000), either continuously or through traditional gravimetric technique, and the mean value of dust amount collected on the membranes was utilized as a correction factor to be applied to continuously collected data. PM10 concentration amount incoming from inlets was removed from PM10 emission calculation, to estimate the real contribution of pig house dust pollution into atmosphere. Mean yearly emission factor of PM10 was measured in 2 g d-1 LU-1 for the weaning room, 0.09 g d-1 LU-1 for the farrowing room, 2.59 g d-1 LU-1 for the fattening room and 1.23 g d-1 LU-1 for the gestation room. The highest PM10 concentration and emission per LU was recorded in the fattening compartment while the lowest value was recorded in the farrowing room. CO2, CH4 and N2O concentrations were continuously measured in the exhaust ducts using an infrared photoacoustic detector IPD (Brüel & Kjaer, Multi-gas Monitor Type 1302, Multipoint Sampler and Doser Type 1303) sampling data every 15 minutes, for the 60 % of the cycles. Yearly emission factor for CO2 was measured in 5997 g d-1 LU-1 for the weaning room, 1278 g d-1 LU-1 for the farrowing room, 13636 g d-1 LU-1 for the fattening room and 8851 g d-1 LU-1 for the gestation room. Yearly emission factor for CH4 was measured in 24.57 g d-1 LU-1 for the weaning room, 4.68 g d-1 LU-1 for the farrowing room, 189.82 g d-1 LU-1 for the fattening room and 132.12 g d-1 LU-1 for the gestation room. Yearly emission factor for N2O was measured in 3.62 g d-1 LU-1 for the weaning room, 0.66 g d-1 LU-1 for the farrowing room, 3.26 g d-1 LU-1 for the fattening room and 2.72 g d-1 LU-1 for the gestation room. |
| Uncertainties expressed as 95% confidence limit: | Upper: [A] 0.081; [B] 4.558; [C] 0.192; [D] 0.600 Lower: [A] 0.039; [B] 0.542; [C] 0.108; [D] 0.200 |
| Data quality: | - |
| Distribution shape: | Normal |
| Data quality reference: |  |
| Other info on data quality: |  |

| Usage/Review information |
| --- |
| Type of parameter: | Measured |
| Measurement technique/standard: | For dust: near forward light scattering (Haz Dust EPAM 5000, SKC); for gases : IPD (Photacustic detector, Bruel and Kiaer) |
| Periodicity of measurement: | Yearly (day by day, with a frequency rate of 1 min) |
| External quality control performed: | Peer reviewed |
| Date of measurement: | November 2005- November 2006 |
| Comments from the data provider: | 1. N2O emission was measured as concentration in the building with the aim to calculate emission factors from a mechanical ventilated animal building. 2. All the nitrous oxide emissions have been attributed to the manure management. |
| Comments from others: |  |
| Link: |  |